## Slide 1: Parameterization of a RIBASIM model and the network lumping approach
Practical application of RIBASIM
Delft, 2023-11-28
Harm Nomden

## Slide 2: Practical application of RIBASIM
Content  Challenges / Questions:
RIBASIM in general:
  What do they mean with ‘basins’?
  At which resolution do you want to calculate?
Setup modelling schematisation:
  How can I create/define ‘basins’?
  How do I fill required settings with data?
Comparison results:
  Are the modelling results good (enough)?
  What are the calculation times?
Harm Nomden
Consultant Hydrology at Sweco (Netherlands)
Background:
  10 yrs international projects and automatisation (python)
  Since 2022 working in the Netherlands
For the TKI project on RIBASIM:
We have been working on a python toolbox ribasim-lumping focusing on generation of RIBASIM-model

## Slide 3: RIBASIM-lumping: Pilot De Hooge Raam (Aa en Maas)
Detailed D-HYDRO model available with 2500 calculation points

## Slide 4: RIBASIM-lumping: Network lumping
1
1
1
1
1
1
1
2
2
2
2
2
2
2
2
3
3
3
3
4
4
2
1
3
4
2
1
3
Definition
split-locations
(split_nodes)
Conversiontable split-locations  Ribasim-nodes
Typical split-locations are weirs or pumping stations, culverts, orifices or other structures or open water connections

## Slide 5: split nodes: 1 weir > 2 basins

## Slide 6: split nodes: 4 weirs - 5 basins

## Slide 7: split nodes: 9 weirs - 10 basins

## Slide 8: split nodes: 14 weirs - 15 basins

## Slide 9: split nodes: 24 weirs - 25 basins

## Slide 10: split nodes: 57 weirs - 58 basins

## Slide 11
4 weirs
9 weirs
14 weirs
24 weirs
57 weirs
1 weir

## Slide 12: RIBASIM-lumping: Deriving relations
stuw
discharge area units
network
reference point basin
TabulatedRatingCurve
Basin area
Basin
Model/Data
RIBASIM
Openwater connections: Exchange based on waterlevel difference – Manning-node
Level controlled areas: Horizontal water level in basin – Pump/Outlet
Sloping area / free flowing: Backwatercurve – TabulatedRatingCurve
H-H relation: Waterlevel-Waterlevel – Water level basin versus water level within basin
V-H relation: Volume-Waterlevel – Storage curve basin
Q-H relation: Discharge-Waterlevel – Outflow from basin to other basin

## Slide 13: RIBASIM-lumping: Deriving input relations
stuw
discharge area units
network
reference point basin
TabulatedRatingCurve
Basin area
Basin
Model/Data
RIBASIM
reference point basin
weir
H-H relation
distance [m]
weir height

## Slide 14: RIBASIM-lumping: Deriving input relations
reference point basin
weir
H-H relation
Add x additional profiles based on vertical interpolation
Modelling results: 0,05xMA tot 2,00xMA
distance [m]
stuw
discharge area units
network
reference point basin
TabulatedRatingCurve
Basin area
Basin
Model/Data
RIBASIM
weir height

## Slide 15: RIBASIM-lumping: Deriving input relations
V-H relation
Vbasin
m3
0
Hweir,upstream
reference point basin
weir
H-H relation
Add x additional profiles based on vertical interpolation
Modelling results: 0,05xMA tot 2,00xMA
distance [m]
weir height
Q-H relation based on model results
Q-H relation
Qweir
0
m3/s
Hweir,upstream
Storage curve based on model results
m+NAP
m+NAP

## Slide 16: RIBASIM-lumping: Deriving input relations
reference point basin
distance [m]
Vbasin
0
m3
0
m+NAP
weir
Hreference point, basin
weir height
Hweir,upstream
Qbasin
m3/s
Hreference point, basin
Hstuw,upstream
Translation to reference point
V-H relation
H-H relation
Q-H relation
m+NAP

## Slide 17: Output RIBASIM

## Slide 18: Comparison output D-HYDRO vs RIBASIM

## Slide 19: Comparison output D-HYDRO vs RIBASIM
Simulation results are comparable for every number of basins, because we used a spatially averaged drainage
More spatial variability: rainfall, altitude, slope, soil, landuse  higher detail and more basins

## Slide 20: Practical application of RIBASIM
Content  Challenges / Questions:
RIBASIM in general:
  What do they mean with ‘basins’?
  At which resolution do you want to calculate?
Setup modelling schematisation:
  How can I create/define ‘basins’?
  How do I fill required settings with data?
Comparison results:
  Are the modelling results good (enough)?
  What are the calculation times?
Solutions / Answers:
water system/network divided in parts
Resolution is dynamic (user-specified) or
Definition of split nodes (generates a RIBASIM network using tooling)
Data from database or from stationary modelling results
Discharge and waterlevels comparable with D-HYDRO model
Simulation length | D-HYDRO | RIBASIM | 
Peak discharge 3 days | 29 minutes | 10 basins | 9 seconds
 |  | 58 basins | 12 seconds
1 year | ?? | 58 basins | 53 seconds
Open source python package to set-up
a schematisation: github  ribasim_lumping